## Slide 1: Specialize Parking Oriented Technology (S.P.O.T.) Senior Design Project June 4, 2018
Team Members:
Ramsey Ghanaim
Jonathan Lam
Mario Cabrera
Travis Rogers

## Slide 2: Problem Statement
Our goals for SPOT is to create a modern Parking Management System that is:
  Low powered for each parking unit
  Intuitive and convenient for users
  Simple to use for parking administrators
    Track lot usage and manage user credentials
Our objective is to improve upon the current UCSC parking system by including:
  An easier way to find parking via mobile app
  An automated way to verify/pay for parking with or without permits
  An administrator tracking system
  Real-time parking status updates

## Slide 3: Project Requirements
Hardware
SoftwarE
Scalable
  Allow software to be used in a variety of different parking sizes.
  Support 10 simultaneous sensor connections
Easy to Use
  Intuitive user experience for mobile app
    Users can monitor parking lot statuses
  Simple administrative website
3
Spot unit
  Proximity sensor, Bluetooth, and LEDs to communicate with users
  Wifi interface to connect with gateway and system
Efficient
  Easy to use for users
  Scalable
  Low power

## Slide 4: Our Approach
What technologies do we use?
  Google Cloud Platform’s App Engine
    Scalable Server
  Ti Simplelink 3220S
    Low power microcontroller
    Built-in Wifi
  HC-SR04 Ultrasonic Sensor
    Low power and low cost sensor
  Adafruit Bluefruit LE Bluetooth Beacon
    Low power and easy to program
    User identifies their spot with a Mobile App
  Raspberry Pi
    Gateway between Sensors and App Engine (Scalable and
    minimizes connections to the App Engine)
    Powerful enough to use threads, but low enough to consume less power than a PC
  Android Studio
    Mobile App
  Administrator Website
    Admins can manage parking and user accounts
4

## Slide 5
S.P.O.T. Sensor
Power management
Body design
  Acrylic design is cheap and sturdy
  4 ft tall so users can see LEDs from car
  Sensor 30" from the ground to detect most cars
Ultrasonic sensor to detect car
  Assume a car after 5 seconds
  ~ 3ft range for sensor
LEDs to communicate with user
  Colors indicate spot status
  RGB: illegal, closed, busy
Bluetooth beacon to connect to user's app
  Turns on when spot is busy only
Wifi to connect to gateway
  Network socket messages for spot status
  Heartbeat messages and event messages

## Slide 6
Sensor Flow Diagram

## Slide 7
Power Consumption
Assumptions:
  13 hour workday
  Microcontroller on for 1 second, followed by 3 seconds of sleep
  30 second average user verification where the MC/Bluetooth Beacon must be on
  Unit draws between 15 to 350 mA of current depending on activity
  3,000 mAh battery (2 sets of 3 AA batteries in parallel)

## Slide 8
Gateway Implementation
Forward status's from SPOT sensor to the App Engine
Forward LED statuses from App Engine to SPOT sensors
HTTPS messages to the App Engine are formatted as JSON objects
Reliability
  Make messages re-send if not sent properly
  Have Sensors consistently “check in” with the Gateway to keep track of broken SPOT sensors
Start
accept() Wait and accept incoming connections
Max threads in use?
pthreadCreate() Wait and accept incoming connections
Pthread_join() Wait for one thread to complete
No
Yes
Determine Message type
Send to App Engine
checkIn =2
Forward App Engine response to SPOT Sensor
Log spot check in
checkIn = 1
Make sure all sensors checked in
msg =“timer”

## Slide 9
Google App Engine - Web Application
Connectivity between system components
Purpose:
  Manages status changes for spots
    Updates SQL database
  Verifies users through the mobile app
    Payments
    Permit Enforcement
  Tracks transaction and spot occupation history

## Slide 10
Google App Engine - Implementation
Information sent through HTTP GET/POST messages
  Data encoded in JSON objects
  Gateway, Mobile App, Website
App Engine forwards messages to custom HTTP handlers
Hosts admin website and provides functionality
Verify POST
User Info
Update POST
Sensor Updates
Payment POST
User Info
Update GET
LED Status

## Slide 11
Mobile App - User Interface and Layout
Activities
  Each activity contains its own data and functions
  Usually isolated from other activities in terms of functionality
  Currently have one specific activity to hold core processes within the app (HTTPS and Bluetooth)
Fragments
  An extension of an activity
  Behaves similarly to an activity, also isolated
  We utilize fragments to provide app navigation while still maintaining HTTPS and Bluetooth functionality
Main Activity
Fragment 1
Fragment 2

## Slide 12
Log Out
Navigation
Drawer
Scan for
Beacons
Mobile App - Main Activity
HTTPS POST and GET requests
  Utilize the android Volley library rather than the standard method
    Using the volley is a faster protocol with many requests being called at once
  Handles all communication between the database and the mobile app
Bluetooth Scanner
  Utilize the standard Bluetooth Adaptor library
  Reads iBeacon formatted Bluetooth low-energy devices
  Can read multiple beacons at once

## Slide 13
Mobile App - Permit Verification/Payment

## Slide 14
Navigation Drawer
Account Fragment
Mobile App - User Interface and Layout
Settings Activity

## Slide 15
Mobile App - Login Activity
POST requests
  sendLoginVerify() calls to .../login
    Checks user credentials with the Google Database
  reqeustAccountInfo() calls to .../mobileInfo
    Pulls all user info after login is successful
saveInfo()
  Saves information to sharedPreferences
  Information is accessed solely through sharedPreferences
Isolated from the rest of the app

## Slide 16
Administrator Website
Live view of Parking Spaces
  Clicking on a space shows more details (User credentials)

## Slide 17
Administrator Website
Edit Account Information

## Slide 18
Administrator Website
View transaction and occupation history

## Slide 19: Spring Quarter Results
Everything is functional!
What could be improved on?
  Implement solar panels to further increase battery life.
  Camera for license plate recognition
  Graph Analytic Data
  Google Pay and Apple Pay support