## Slide 1: Specialized Parking Oriented Technology (S.P.O.T.) Senior Design Project June 15, 2018
Team Members:
Ramzey Ghanaim
Jonathan Lam
Mario Cabrera
Travis Rogers

## Slide 2: Motivation
UCSC has an inefficient parking system
  Never know when parking lots are full
  Takes time to travel between parking lots to check availability
  R permits will no longer be valid at North Remote Lot by September 1
We want to modernize the parking system both for users and parking administration

## Slide 3: Problem Statement
Our objective is to improve upon the current UCSC parking system by including:
  An easier way to find parking via mobile app
  An automated way to verify/pay for parking with or without permits
  An administrator tracking system
  Real-time parking status updates
Our goals for SPOT is to create a modern Parking Management System that is:
  Low powered for each parking unit
  Intuitive and convenient for users
  Functional for parking administrators

## Slide 4: Project Requirements
Hardware
SoftwarE
Scalable
  Allow software to be used in a variety of different parking sizes
Easy to Use
  Intuitive user experience for mobile app
    Users can monitor parking lot statuses
  Simple administrative website
4
Spot unit
  Proximity sensor, Bluetooth, and LEDs to communicate with users
  Wifi interface to connect with gateway and system
Efficient
  Easy to use for users
  Scalable
  Low power

## Slide 5: Our Approach
What technologies do we use?
  Google Cloud Platform’s App Engine
    Scalable Server
  SPOT Sensor
    A low cost, low power sensor to detect and report a spot status
  Gateway
    Middle-man between Sensors and App Engine
  Mobile App
    Check parking lot usage
    Verify your permit when parking
  Administrator Website
    Admins can manage parking lots and user accounts
5

## Slide 6
S.P.O.T. Sensor
Power management
Body design
Ultrasonic sensor to detect car
LEDs to communicate with user
Bluetooth to connect to user's app
Wifi to connect to gateway

## Slide 7
Power Consumption
Assumptions:
  13 hour workday
  Microcontroller on for 1 second, followed by 3 seconds of sleep
  20 second average user verification where the MC/Bluetooth Beacon must be on
  Unit draws between 2 to 10 mAh per day depending on activity
  3,000 mAh battery (3 AA batteries in series)
  One year battery life on an average day (10 events per day)

## Slide 8
Gateway Implementation
Purpose:
  Combine traffic to send in one connection to the App Engine to allow this project to scale.
Forward status's from SPOT sensor to the App Engine
Forward LED statuses from App Engine to SPOT sensors
Reliability
  Make messages re-send if not sent properly
  Have Sensors consistently “check in” with the Gateway to keep track of working SPOT sensors

## Slide 9
Google App Engine - Web Application
Connectivity between system components
Purpose:
  Manages status changes for spots
    Updates SQL database
  Verifies users through the mobile app
    Payments
    Permit Enforcement
  Tracks transaction and spot occupation history

## Slide 10
Google App Engine - Implementation
Information sent through HTTP GET/POST messages
  Data encoded in JSON objects
  Gateway, Mobile App, Website
App Engine forwards messages to custom HTTP handlers
Hosts admin website and provides functionality
Verify POST
User Info
Update POST
Sensor Updates
Payment POST
User Info
Update GET
LED Status

## Slide 11
Log Out
Navigation
Drawer
Scan for
Beacons
Mobile App - Overview
Purpose:
  Check number of available parking spaces per lot
  Verify your parking permits and parking payments
Bluetooth Scanner:
  App communicates with the SPOT unit using Bluetooth
  Confirms parking status and parking location

## Slide 12
Navigation Drawer
Account Page
Mobile App - User Interface and Layout
Login Page

## Slide 13
Mobile App - Parking Process
Source: honda.com

## Slide 14
Mobile App - Permit/Payment Process

## Slide 15
Administrator Website
Live view of Parking Spaces
  Clicking on a space shows more details (User credentials)

## Slide 16
Administrator Website
Edit account Information and add new accounts

## Slide 17
Administrator Website
View transaction and occupation history

## Slide 18: Results
SPOT accomplishments
  Long lasting sensors units to verify parking spots
  Easy to use mobile app for spot verification
  Admin website for parking administration
  Cloud infrastructure for scalability
What could be improved on?
  Implement solar panels to further increase battery life
  Camera for license plate recognition
  Analytics

## Slide 19: Thank You